## Slide 1: Advances in GNSS Equipment
Todd Humphreys
With Input From:
Thomas Pany, Bernhard Riedl IFEN, Carsten Stroeber UFAF
Larry Young, JPL
David Munton, UT/ARL
2010 IGS Workshop, Newcastle Upon Tyne

## Slide 2
Q: What advances in GNSS receiver technology can the IGS exploit to improve its network and products?

## Slide 3: Outline
Review conclusions from Miami 2008
A look at commercial receiver state-of-the-art
Advances in software receiver technology
  DFE: The final front-end
  The CASES receiver
  The IFEN/UFAF SX-NSR receiver: Performance evaluation
Not all observables are created equal
Summary

## Slide 4: Conclusions from Miami 2008
Many excellent commercial RXs to choose from
All major manufacturers have road maps toward all-in-view capability
Pseudorange and phase measurement error statistics are heterogeneous and ill-defined, impairing IGS products
Software receivers show promise but have not been vetted

## Slide 5: The Super Receiver
Tracks all open signals, all satellites
Tracks encrypted signals where possible
Well-defined, publicly disclosed measurement characteristics (phase, pseudorange, C/No)
RINEX 3.00 compliant
Completely user reconfigurable, from correlations to tracking loops to navigation solution
Internal cycle slip mitigation/detection
Up to 50 Hz measurements
Internet ready; signal processing strategy reconfigurable via internet
Low cost

## Slide 6: The Ultra Receiver
Software
Correlators
Tracking
Loops, Data
Decoding,
Observables
Calculations
FFT-based
Acquisition
Software Post-Processing
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock

## Slide 7: Commercial Receiver Offerings (2008)
Topcon NET-G3
Trimble NetRS/NetR5
Septentrio PolaRx3
Leica GRX1200

## Slide 8: Commercial Receiver Offerings (2010)
Topcon NET-G3
Trimble NetRS/NetR5/NetR8
Septentrio GeNeRx1
Leica GRX1200+GNSS
Javad G3T

## Slide 9: Receiver Type Distribution (June 2010)
Chart: 
| AOA BENCHMARK ACT | AOA SNR | ASHTEC (all) | BLACKJACK | JAVAD G3T | JPS | LEICA GRX1200 | LEICA RS | NOVATEL | ROGUE SNR | SEPTENTRIO | TPS | TRIMBLE NET | TRIMBLE (other)
 | 12 | 6 | 117 | 1 | 1 | 36 | 56 | 1 | 5 | 4 | 8 | 36 | 62 | 15
Fastest Growth Since 2007

## Slide 10: Approaching the Super Receiver
Tracks all open signals, all satellites
Tracks encrypted signals where possible
Well-defined, publicly disclosed measurement characteristics (phase, pseudorange, C/No)
RINEX 3.00 compliant
Completely user reconfigurable, from correlations to tracking loops to navigation solution
Internal cycle slip mitigation/detection
Up to 50 Hz measurements
Internet ready; signal processing strategy reconfigurable via internet
Low cost
Example Commercial Reciver: Javad G3T
Except E5B,
216 channels
Loop BW, update rate configurable
~$8k
Only one G3T in IGS network (BOGI, Poland)
Performance appears good

## Slide 11: Outline
Review conclusions from Miami 2008
A look at commercial state-of-the-art
Advances in software receiver technology
  DFE: The final front-end
  The CASES receiver
  The IFEN/UFAF SX-NSR receiver: Performance evaluation
Not all observables are created equal
Summary

## Slide 12: Recall: The Ultra Receiver
Software
Correlators
Tracking
Loops, Data
Decoding,
Observables
Calculations
FFT-based
Acquisition
Software Post-Processing
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock

## Slide 13: The ARL:UT Digitizing Front End

## Slide 14: The ARL:UT Digitizing Front End
(Fig. 1 of Wallner et al., "Interference Computations Between GPS and Galileo," Proc. ION GNSS 2005)
1130 MHz
1630 MHz
500 MHz span

## Slide 15: The ARL:UT Digitizing Front End
500 MHz bandwidth
Single RF signal path and ADC substantially eliminates inter-signal instrument biases
Temperature-stabilized signal conditioning chain
Open-source design, as with GPSTk
Debut at ION GNSS 2010

## Slide 16: UT/Cornell/ASTRA CASES SwRx
V0
V1
V2

## Slide 17: UT/Cornell/ASTRA CASES SwRx
V3
Dual-frequency narrowband
Completely software reconfigurable
Antarctic deployment 2010
Space deployment 2012
(as occultation sensor)

## Slide 18: CASES Multi-System Receiver Bank

## Slide 19: Approaching the Ultra Receiver
Software
Correlators
Tracking
Loops, Data
Decoding,
Observables
Calculations
FFT-based
Acquisition
Software Post-Processing
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock
Digital Storage Rx
Mass Storage
RF Front-End
Reference Oscillator
ADC
Sample Clock

## Slide 20: Approaching the Ultra Receiver
Mass Storage

## Slide 21: Multicore GNSS Processing
Signal-type level
  Low comm/sync overhead
  Poor load balancing
Channel level
  Low comm/sync overhead
  Good load balancing
  Favors shared memory architecture
Correlation level
  Higher comm/synch overhead
  Good load balancing
Sub-correlation level
  Very high comm/synch overhead
  Good load balancing
Demonstrated 3.4x speedup on 4-core machine with OpenMP
CASES post-processing now 25x real-time
Bodes well for reanalysis

## Slide 22: UFAF SwRx Evaluation (Carsten Stroeber)
Advantages
Extensive data analysis possible at measurement time
  e.g. instantaneous monitoring for signal distortions with access to “low” level measurements i.e. signal sample data
Software receiver is “independent” from utilized hardware
Running since | End 2007
Current Signals | GPS L1 C/A, L2C (CM+CL), L5 Giove A+B SBAS
Frontend | Fraunhofer, (IFEN possible)
Longest running time without external reset | >10 days
Longest running time with external reset | >1 month
Annotations:
External reset denotes automatic restart of the receiver via script program
Reference station was on a productive system simultaneously employing monitoring algorithms -> priority was not only given to long time stability
Currently Glonass is in test mode
Dedicated software receiver reference station (GPS L1, L2 only) intended for long run stability is in test phase
http://www.unibw.de/lrt9_3

## Slide 23: UFAF SwRx Evaluation
Horizontal scatter plot of final PDGPS adjustment at highest temporal resolution with bounding box (upward: north; right: eastward).
Date | DoY 170, Year 2007
Analysis Software | PrePos GNSS Suite
Measurements | GPS L1
Number observations (double differences) | 128614
Duration | 405 min
Data deleted due to cycle slips | 2% (for OEM 4 receiver 1%)
Standard deviation position | X 5.2mm Y 3.7mm Z 6.1mm

## Slide 24
Coordinate time series of final PDGPS adjustment. Software receiver at top, OEM IV at bottom.
Operational performance comparable to NovAtel OEM 4

## Slide 25: UFAF SwRx Evaluation
Drawbacks, suggested directions
Complex interaction between PC hardware, working system, additional applications and software receiver e.g.:
  USB access is controlled by working system (drivers …) -> buffering needed
  Additional applications starts unmeant, process time consuming action e.g. disk defrag -> additional applications must be deleted or configured too
Short-time internal processing load peaks due to frequently simultaneous execution of extensive tasks -> 2 strategies:
  For reference station no “real” real-time needed -> use already existing buffering
  Adapt configuration to PC hardware and use high power hardware
Free configurability leads to a big error source given by non optimal or wrong configuration -> in reference station mode this is relaxed due to fixed configuration

## Slide 26: Outline
Review conclusions from Miami 2008
A look at commercial state-of-the-art
Advances in software receiver technology
  DFE: The final front-end
  The CASES receiver
  The IFEN/UFAF SX-NSR receiver: Performance evaluation
Not all observables are created equal
Summary

## Slide 28: Toward a Standardized Carrier Phase and Pseudorange Measurement Technique
Different receiver manufacturers use proprietary (code/carrier) measurement definitions
Standard proposed by L. Young at last IGS workshop based on the US patent no. 4,821,294 (Thomas, Jr., Caltech)
Goal: to have stochastically independent code/carrier observations with a well understood observation principle
Use SX-NSR software receivers API for a prototype implementation

## Slide 29: Illustration (Carrier Phase)
‘Verification’ that correlator based observations are truly independent
Download: C++ source code and exemplary data (GPS L1, Galileo E1/E5a) at www.ifen.com
GPS C/A PRN13
Week 1570, sec ~
234179, NavPort-2
Frontend with OCXO

## Slide 30: Illustration (Pseudorange)
GPS C/A PRN13
Week 1570, sec ~
234179, NavPort-2
Frontend with OCXO

## Slide 31: Evaluating the Example
Code minus carrier analysis shows that data is statistically independent
Discriminators cancel time correlation caused by the low bandwidth (0.1 -0.25 Hz) tracking loops
Phase discriminiator unwrapping together with FLL tracking gives valid carrier ranges

## Slide 32: Summary
Q: What advances in GNSS receiver technology can the IGS exploit to improve its network and products?
  A1: Commercial receivers are approaching the “Super Receiver”: nearing all-GNSS-signals tracking, reconfigurable, low-cost
  A2: 500-MHz digitizing open-design front-end captures all current and planned GNSS signals, substantially eliminates inter-signal RX biases
  A3: 500-MHz front-end + Multi-system SwRx + Multi-core processing + data buffering  Ultra Receiver
  A4: SwRx performance comparable to commercial geodetic RXs (but not yet as reliable)
  A5: Receiver APIs offer path for measurement standardization (e.g., IFEN SX-NSR)