## Slide 1: An Evaluation of the Vestigial Signal Defense for Civil GPS Anti-Spoofing
Kyle Wesson, Daniel Shepard, Jahshan Bhatti, and Todd Humphreys
Presentation at ION 2011| September 22, 2011

## Slide 2: Acknowledgements

## Slide 3: Outline
Civil Anti-Spoofing Overview
Interference Model
Video Comparison: Interference
Interference Detection Metrics
Ongoing Work

## Slide 4: Types of Civil Anti-Spoofing
Civil Anti-Spoofing
Cryptographic
Security-Enhanced GPS
(NMA or SCA)
Non-Cryptographic
Dual-Receiver Correlation
Multi-Antenna Defense
Vestigial Signal Defense (VSD)
Why VSD?
Implementable today!
Software-only defense; requires no additional receiver hardware
Why not cryptographic anti-spoofing?
Requires infrastructure and possibly changes to GPS IS
Vulnerable to initial phase of spoofing attack

## Slide 5: What is the Vestigial Signal Defense?
FACT: Suppressing authentic GPS signal during a spoofing attack is difficult
OPPORTUNITY: Ad-mixture of spoofing and authentic GPS signal can lead to detectable corruption of the complex correlation function
PROBLEM: Interaction of spoofing and authentic GPS signal is similar to interaction of multipath and direct-path GPS signal
DEFINITION: VSD is a technique for monitoring distortion in the complex correlation function
VSD Goal: Reduce the degrees-of-freedom available to a spoofer, making it mimic multipath (i.e., “corner in” the spoofer)

## Slide 6: Interference Model
Direct Path:
Multipath:
Spoofing:

## Slide 7: Visual: Complex Correlation Domain

## Slide 8: Interference Comparison: The Tools
The Multipath Monitor (GCAF)
500 MHz bandwidth
512 Correlation Tap Dump at 1000 Hz
Designed at UT Applied Research Labs
Debut at ION GNSS 2010
The Spoofer
Real-time civil GPS spoofer
Enables civil anti-spoofing research
Described in open-literature
Debut at ION GNSS 2008
loaned by University of Texas Applied Research Laboratory

## Slide 9: Multipath Wardriving Campaign
1) NI RFSA can record 30 MHz bandwidth about GPS L1 frequency slaved to OCXO clock
2) Loaded test equipment into truck and recorded data in downtown Austin, Texas
3) Post-processed data with software-defined GPS receiver

## Slide 10: Test Setup
Spoofer
Multipath Record/Playback
GCAF

## Slide 11: Complex Correlation Domain Explanation

## Slide 12: Is it Spoofing or Multipath?

## Slide 13: Videos

## Slide 14: Observations
Multipath can look like spoofing!
Spoofing can look like multipath!
Detecting the difference between spoofing and multipath is difficult!

## Slide 15: Proposed Spoofing Detection Metrics
Sensible Suggestion: Apply signal quality and multipath monitoring metrics to spoofing detection:
Delta-Test [1]:
Ratio-Test [1,2,3]:
[1] Ledvina, B.M. et al., “An In-Line Anti-Spoofing Device for Legacy Civil GPS Receivers,” (2010) Institute of Navigation ITM, San Diego, CA.
[2] Cavaleri, A. et al., “Detection of spoofed GPS signals at code and carrier tracking level," (2010) Satellite Navigation Technologies and European Workshop on GNSS Signals and Signal Processing (NAVITEC).
[3] Cavaleri, A. et al., “Signal Quality Monitoring Applied to Spoofing Detection,” (2011) ION GNSS, Portland, OR. [Session C3, Paper #1]

## Slide 16: Examining the Ratio Test (1/3)
Mean = 0.42
Std = 0.011
PF= 5.7e-7

## Slide 17: Examining the Ratio Test (2/3)
Mean = 0.43
Std = 0.009
PF= 5.7e-7
Corresponds to Video

## Slide 18: Examining the Ratio Test (3/3)
Mean = 0.47
Std = 0.021
PF= 5.7e-7
Corresponds to Video

## Slide 19: Takeaways
Possible high false alarm rate if no reliable method to differentiate spoofing and multipath
Most metrics ignore quadrature component
Certain taps may be better discriminators than others

## Slide 20: Ongoing Work
Maximum-likelihood {α, τ, θ} tracking:
Bistatic-radar-based localization of interference sources
Tertiary hypothesis tests on α

## Slide 21: Conclusions
Multipath can look like spoofing!
Spoofing can look like multipath!
Blind application of signal quality monitoring may lead to a high false alarm rate
VSD is still under development
Goal: reduce the degrees-of-freedom available to a spoofer, making it mimic multipath
Multipath and Spoofing Data Set Available:
http://radionavlab.ae.utexas.edu